## Slide 1: Autonomous Drone Engineer C2 – Network and ssh
Paul.Guermonprez@intel.com Autonomous Drone Solutions Architect

## Slide 2: Local wireless connectivity
By default, Intel Aero is acting as Wifi access point. It is convenient for the initial calibration and QGC user interface.
Access point name is “Aero-*” where * is the mac address of your drone
Password is “1234567890”
You can connect your development station to this network
Then launch ssh on IP 192.168.8.1, login is ”root”, no password
You can access Intel Aero over the access point included. But the Drone is NOT connected to Internet.

## Slide 3: Local USB connectivity
If you plug a direct micro USB Cable between your PC and Intel Aero, it will create a USB-ethernet adapter and allocate an IP address for your PC.
You can then access Intel Aero over this USB cable with IP 192.168.7.2
Note: each OS and installation has different ways to handle networking. This method may interfere with your setup (ex: network-manager on Ubuntu). It is an advanced method. That’s why we recommend you use the wireless method (see next slide).
You can access Intel Aero with USB-ethernet. But it’s an advanced method, use the wireless method instead.

## Slide 4: Internet wireless connectivity
By default, Intel Aero is acting as Wifi access point but for development, you’ll want to connect Intel Aero to your Wifi network, to access internet, install packages and access Aero remotely from your development computer.
This action is done using the keyboard, mouse and screen connected to Intel Aero (or with the USB-ethernet method). After this step, you’ll access Aero remotely and won’t need them anymore.
For details, consult: https://github.com/intel-aero/meta-intel-aero/wiki/08-Aero-Network-and-System-Administration#networking-internet-access

## Slide 5: What Intel Aero’s IP?
If you are still in Wifi access point mode, it’s 192.168.8.1
If you joined your Wifi network as client, it’s been allocated by your DHCP server (see the DHCP section of your router/access point).
While you are still connected to Aero with the HDMI screen and keyboard run the command “ip addr” to get your IP. Ex: On my network it’s 192.168.1.105
You can ask your system administrator to make a DHCP reservation to have a constant IP.

## Slide 6: ssh connectivity
Once Intel Aero is connected to the same network as our development station, we can connect remotely with ssh, copy files with scp.
On Windows, you can use putty for ssh and filezilla for scp.
On Mac and Linux, it’s included.
Set a new password!
You’re now connected over ssh

## Slide 7: Development methods
You can edit your source files, compile and execute remotely on Intel Aero over ssh. As an example: vi, python, make, gcc are included.
It is also possible to edit sources on your station and transfer them to Intel Aero for execution.
In this capture, I used IDLE editor on Mac, transferred the file with scp and executed on Aero.

## Slide 8: Conclusion
We:
Connected Intel Aero to our Wifi network
Discovered connmanctl, a powerful networking tool
Have ssh access from our workstation
Can edit, compile, execute
We’re ready to code!

## Slide 9: Thanks
Paul.Guermonprez@intel.com