## Slide 1: Autonomous Drone Engineer D1 – Hello World – Motor Control
Paul.Guermonprez@intel.com Autonomous Drone Solutions Architect

## Slide 2: Architecture Summary
To summarize the software architecture described in the module B4:
Flight Controller and Compute Board are linked with a serial port
The protocol is the standard MAVLINK
A proxy is exposing this serial port as a network socket on port 5760
Connect your code to the socket 5760 with tcp using the MAVLINK protocol
Yocto Linux running on Intel Aero Compute Board
PX4 or Ardupilot running on Intel Aero Flight Controller
Serial Port
MAVLINK Proxy
Drone Software running on Yocto
Local Port 5760

## Slide 3: Hello World – Python-MAVLINK

## Slide 4: Hello World in Python-MAVLINK
While connected as root on Intel Aero, Aero being connected to Internet:
Get the code from Intel’s github repository: git clone https://github.com/01org/mavlink-router.git cd mavlink-router/
and execute a simple example: python examples/heartbeat-print-tcp.py 127.0.0.1:5760
you’ll see messages like: HEARTBEAT {type : 2, autopilot : 12, base_mode : 29, custom_mode : 84148224, system_status : 3, mavlink_version : 3} HEARTBEAT {type : 2, autopilot : 12, base_mode : 29, custom_mode : 84148224, system_status : 3, mavlink_version : 3}
You’re connected to the flight controller!

## Slide 5: Hello World in Python-MAVLINK
We’re using the mavlink library in Python: pymavlink (already installed)
import pymavlink.mavutil as mavutil
We’re connected to the local IP with a tcp socket on port 5760 (I’m replacing sys.argv[1] by it’s value):
mav = mavutil.mavlink_connection('tcp:127.0.0.1:5760')
Waiting for heartbeat:
mav.wait_heartbeat()

## Slide 6: Arming Motors in Python-MAVLINK
IMPORTANT: REMOVE THE PROPELLERS FROM THE MOTORS FIRST
Edit the previous file heartbeat-print-tcp.py, add “import time” to the required imports, then add after the wait_heartbeat the 2 following lines: ARM and DISARM mav.mav.command_long_send(mav.target_system, mav.target_component, mavutil.mavlink.MAV_CMD_COMPONENT_ARM_DISARM,0,1,0,0,0,0,0,0) time.sleep(5) mav.mav.command_long_send(mav.target_system, mav.target_component, mavutil.mavlink.MAV_CMD_COMPONENT_ARM_DISARM,0,0,0,0,0,0,0,0)
You’re spinning the motors for 5 seconds

## Slide 7: Summary of Python-MAVLINK
Summary:
Use TCP sockets on port 5760
After the initial connection, wait for the first heartbeat
In MAVLINK, messages are endoded as frames
Frames have names: MAV_CMD_COMPONENT_ARM_DISARM
And arguments (here it’s 1 for ARM, 0 for DISARM)
The MAVLINK library is easy to use
There’s interfaces for Python but also other languages

## Slide 8: Hello World – Python-DroneKit

## Slide 9: DroneKit
It’s important to know the basics of MAVLINK, as it the base of all communications with the Flight Controllers.
But coding frames with python-mavlink is not developer friendly.
DroneKit, developed by 3D Robotics (http://3drobotics.com), is one of the friendly python abstractions available under Apache v2 Licence : http://python.dronekit.io
To install on Intel Aero:
pip install dronekit

## Slide 10: Hello World in Python-DroneKit
from dronekit import connect, VehicleMode, LocationGlobalRelative import time vehicle = connect('tcp:127.0.0.1:5760', wait_ready=True)
print "Arming motors: " vehicle.mode = VehicleMode("GUIDED") vehicle.armed = True
while not vehicle.armed: print " Waiting for arming to be finished " time.sleep(1)
print "Keeping motors armed for 5s " time.sleep(5)
print "Disarming " vehicle.armed = False

## Slide 11: Summary of Python-DroneKit
Summary:
Using the regular Python-MAVLINK as base
Same connection (tcp 5760) as all the other methods
Developer friendly and well documented: http://python.dronekit.io/guide/index.html

## Slide 12: Hello World – Python-MAVProxy

## Slide 13: MAVProxy
On top of being a developer friendly layer on top of MAVLINK, MAVProxy was designed to bridge the gap between programming-only libraries like DroneKit and graphical-only tools like QGroundControl.
Check: http://ardupilot.github.io/MAVProxy
Some people use it on a remote computer to control the drone, but you an use on the drone itself for autonomous drone development.
To install on Intel Aero:
pip install MAVProxy

## Slide 14: Hello World in Python-MAVProxy
We’re launching the console on Intel Aero:
mavproxy.py --master=tcp:127.0.0.1:5760 --quadcopter
And typing a few commands:
arm throttle disarm bat

## Slide 15: Summary of Python-MAVProxy
Summary:
You can use it locally on Intel Aero as a shell
You can use it remotely on your desktop for maps, joysticks and more
Using the regular Python-MAVLINK as base
Same connection (tcp 5760) as all the other methods
Developer friendly and well documented: http://ardupilot.github.io/MAVProxy/html/

## Slide 16: Thanks
Paul.Guermonprez@intel.com